## Slide 1: Classifying Elephant and Mice Flows in High-Speed Networks
Mariam Kiran
Anshuman Chabbra (NSIT)
Anirban Mandal (Renci)
Presented at INDIS 2017
ESnet, LBNL
Funded under DE-SC0012636

## Slide 2: Talk Agenda
Current challenges in Elephant and Mice flows: Why bother?
Unsupervised machine learning techniques: Why?
Solution: Development of a learning classifier system using GMM
Current state – lessons learned and exploitation of classification results
Evaluation and Future work

## Slide 3: Myth not in Networks! “Elephants scared of Mice”
Data centers and networks get a mixture of flows:
  Elephant flows:
    Large size
    Long-lived
    Large data transfers
    Throughput-sensitive
  Mice Flows:
    Smaller bursty traffic
    Short-lived
    Latency-sensitive
Scientific networks versus data center traffic
  Majority flows: Elephant flows (Big data files)
    Gobbles up network buffers causing queuing delay to mice flows
    Challenges of adaptive routing: Changing paths on-the-go
    Links also have to be optimized: multi-objective problem

## Slide 4: Why should we understand flows?
Our networks is very dynamic.
Losing data or jeopardizing applications prevents us to achieving our mission!
Goal is to detect and then manage

## Slide 5: Previous work
Classify traffic for intrusion detection and traffic profiling
  Number of packets transferred, flow duration, file size
  Papers link tools to perform dynamic traffic steering
    Isolating traffic streams
    Based on size, rate, duration, burstiness, or combination
However real-time detection is a challenge!
  Online (as flow arrives) versus offline analysis (periodic)
S. Shirali-Shahreza et al. Traffic statistics collection with Flexam, in: Proceedings of 2014 ACM SIGCOMM.
T. Zizhong Cao et al. Traffic steering in software defined networks: planning and online routing, SIGCOMM workshop on Distributed cloud computing.
Z. Yan et al. A network management system for handling scientific data flows, Journal of Network and Systems Management 24 (2016) 1–33.
Notes: Isolate science data from general flows
Alpha flows (size and bursitness)
    size (elephant/mice), rate (cheetah/snail), duration (tortoise/dragonfly), burstiness (porcupine/stingray)

## Slide 6: Lets use Netflow Records
Netflow: Collected every 5 minutes (aggregated flows)
  Perfsonar: active testing for health
  Every site is unique: traffic received
Site (1 month) | Mean (size) | Max (size) | Mean (duration)
ROne | 0.15 | 25.6 | 23.19
RTwo | 0.03 | 36.4 | 4.14
RThree | 0.02 | 72.5 | 6.63
6
LBL
FNL
ANL
CRN
PT
PT
(TCP, UDP)
throughput, loss, utilization
Flow first seen Duration Protocol Source IP:Port Destination IP:Port Packets Bytes Flows
2017-04-15 00:00:23.040 TCP 50.127.55.32:3455 -> 137.243.29.226:23 0 40 1
2017-04-15 00:00:23.040 UDP 120.129.253.114:9788 -> 121.127.238.102 0 42 1
2017-04-15 00:00:23.850 UDP 120.129.253.114:9433 -> 121.127.151.25 0 42 1

## Slide 7: Finding elephants and mice in flows
Exploring Netflow data
Cluster traffic into TWO groups with NO prior knowledge
Unsupervised learning: Organize data into clusters based on attribute values:
  Find patterns, relationships, similarity across data

## Slide 8: K-means results
Start with no knowledge and find centroids with closest data points
Target: Form 2 clusters based on size and bytes/s
Results:
  Overlapping data points in clusters
  Algorithm fails due to different density and data size in flows
We need some knowledge in the algorithm
RSite3
Cluster data based on distance

## Slide 9: Gaussian Mixture Model (Semi-supervised)
Scikit-learn python library for GMM-EM (Expectation maximization)
  Only 30 lines of code
  Semi-supervised: Initialize with some knowledge
    Assume 10% elephant and 90% mice and then refine µe=0.1, µm=0.9
    Compute probability of flow belonging to cluster and update µe, µm
    Compute mixture coefficients per site
    Repeat process until converge to a local optimum.
NetFlow data
(per Rsite) Flow size, flow rate
Two Cluster: Elephants and Mice
GMM-EM Algorithm 1. Initialization 2. Expectation
3. Maximization

## Slide 10: Working of GMM-EM algorithm
Flow characteristics are dependent:
  Per site
  Per time of the day
GMM assumes there is a Gaussian distribution of mixture of classes
  Data set is a mixture of elephant and mice flows
Initialization Step: 10% flows are elephant in my traffic (0.1,0.9)
Expectation Step: Compute belonging to a cluster based on Gaussian equations
Maximization Step: Keep re-iterating till converge
Maximum likelihood fit to Gaussian density (red)
Observation data set (green) also called responsibility

## Slide 11: Use Classification to build a LCS
LCS = Learning Classifier System
Each site is different, and flow characteristics change over time
Classifier will find different characteristics of elephants and mice:
  Not have a predefined definition e.g. thresholds
Knowledge Base
Environment
learn
Apply Actions
(Classifier)
Rule-based trigger

## Slide 12: Results

## Slide 13: Semi supervised gives better results
Clear clusters found!
Each site cluster has different characteristics
Blue = Elephant, Orange = Mice
Rsite1 more Elephants flows compared to Rsite2/Rsite3 (higher duration)
Mice flow ranges are different for Rsite3 (based on flow size)
Rsite1
Rsite2
Rsite3

## Slide 14: What lessons did we learn?
Clustering leads to more statistical analysis on what elephants/mice are
Too much Noise in data:
  First few netflow records contained Perfsonar tests,
    being classified as elephant flows, had to be cleaned
Needed some knowledge for semi-supervised:
  Leads to skewed results of elephants lying in top 10% size and rate
  Need an independent verification with ground truth data
    E.g. Simulating GridFTP transfers to see if recognized as elephants
ML BlackBox problem:
  Using ML libraries does not expose internal algorithm workings
  Propose building ‘open’ libraries

## Slide 15: Is Netflow enough?
Initial idea was:
  Can we to Active Traffic Steering using identified clusters?
There is Noise: difficult to recognize
  Link testing data
  No track of congestion on link
  Bad configuration
  Sampling rate can be altered
Additional infrastructure required
  Sflow: Expensive but is it worth it?
More end-to-end data
  Whether flows captured belong to same stream? Interface/port data
  I/O data
Knowledge Base
Environment
learn
Apply Actions
(Classifier)
Rule-based trigger
Notes: If flow parallelized that flow data not tell us.. Go through different ports .. Network doesnt know, but know if we had data from endpoints

## Slide 16: Building Learning classifier system
Knowledge base
Flow record
(1…10)
Action
Training
Learn
Classify
Predict
Divert traffic
Active steering: Netflow data is past data
  Thresholding mechanisms are good approaches!
  Needs more testing for how flows can be isolated
Not do active steering but learn about sites
  how heavy traffic is?
  Add more links, add more infrastructure, fault management
Notes: Learns features probabilities where is think data falls into clusters

## Slide 17: Conclusion
Overall was easy to implement but has its caveats
Focused on online training and learning per site: Unique compared to existing works in area
Processing time is fairly fast
Next steps
  Working through the GMM algorithm to plot how Gaussian mixture changes
  Run real-time tests to see if we can isolate traffic streams based on netflow classification
  Understand flow behavior across sites

## Slide 18: Thankyou
Any Questions?
  We do have an open PostDoc position (ML in Networks)
  Please reach out
  <mkiran@es.net>